## Slide 1
제조사
MODEL
NAME
DPA
4466
HEADSET MICROPHONE
Omnidirectional Headset Microphone
Directional pattern : Omnidirectional
Principle of operation : Pressure
Frequency response : 20 Hz - 20 kHz
Effective frequency range ±2 dB
Soft boost grid : 40 Hz - 20 kHz, 3 dB soft boost at 8 – 20 kHz.
High boost grid : 40 Hz - 20 kHz, 10 dB boost at 12 kHz
Sensitivity, nominal, ±3 dB at 1 kHz : 6 mV/Pa; -44 dB re. 1 V/Pa
Distortion, THD < 1% : 134 dB SPL RMS, 137 dB SPL peak
Dynamic range - CORE : Typ. 111 dB
Max. SPL, THD 10% : 144 dB SPL peak
Rated output impedance : 30 - 40 Ω
Connector : MicroDot, TA4F Mini-XLR, 3-pin LEMO, Mini-Jack
Color : Black or beige
Weight : 12 g (0.4 oz) incl. Cable and MicroDot connector
Microphone diameter : 5.4 mm (0.21 in)
Cable length : 1.3 m (4.3 ft)
Cable diameter : 1.6 mm (0.06 in)