## Slide 1
제조사
MODEL
NAME
LAB.GRUPPEN
E2:2
POWER AMP
2ch POWER AMPLIFIER
Number of channels : 2
Total output all channels driven : 200 W
Peak output voltage per channel : 100 V / 70 Vrms
Max. output current : 7.7 Arms
Max. Output Power (all ch.’s driven)
- 2 ohms : N.R.
- 4 ohms : 100 W
- 8 ohms : 100 W
- 16 ohms : 100 W (requires the “70 V” mode for the RSL, “Lo-Z” gives 50 W)
- 70 V : 100 W
- 100 V : Can deliver 100 W to a 100 V load tapped at 200 W
THD 20 Hz - 20 kHz for 1 W : <0.1%
THD at 1 kHz and 1 dB below clipping : <0.05%
Signal To Noise Ratio : >112 dBA
Channel separation (Crosstalk) at 1 kHz : >70 dB
Frequency response : 2 Hz - 40 kHz
Input impedance : 20 kOhm
Common Mode Rejection (CMR) : 50 dB
Output impedance : 25 mOhm
Dimensions (WxHxD) : 483 x 44 x 276 mm
Weight : 4.2 kg