## Slide 1
제조사
MODEL
NAME
LAB.GRUPPEN
E40:4
POWER AMP
4ch POWER AMPLIFIER
Number of channels : 4
Total output all channels driven : 4000 W
Peak output voltage per channel : 141 V / 100 Vrms
Max. output current : 21.2 Arms
Max. Output Power (all ch.’s driven)
- 2 ohms : 900 W
- 4 ohms : 1000 W
- 8 ohms : 1000 W
- 16 ohms : 625 W
- 70 V : 1000 W
- 100 V : 1000 W
THD 20 Hz - 20 kHz for 1 W : <0.1%
THD at 1 kHz and 1 dB below clipping : <0.05%
Signal To Noise Ratio : >106 dBA
Channel separation (Crosstalk) at 1 kHz : >70 dB
Frequency response : 2 Hz - 40 kHz
Input impedance : 20 kOhm
Common Mode Rejection (CMR) : 50 dB
Output impedance : 25 mOhm
Dimensions (WxHxD) : 483 x 44 x 417 mm
Weight : 7.9 kg